## Slide 1: Adaptive Multicast Suppression
Named Data Networking
Ernest McCracken
University of Memphis

## Slide 2: Interest Multicasting
Under interest and data reply multicasting we can run into scenarios where lots of redundant traffic flows across the network.
A node floods a subnet with an interest and some small amount of time later another node floods the subnet with the same interest.

## Slide 3
Interest for /A
At t = 0ms a node multicasts interest /A.

## Slide 4
Interest for /A
At t = 10ms a second node also multicast interest /A
Node may have already heard the interest for /A being multicasted.

## Slide 5: Data Reply Multicasting
As with Interest multicasting we can run into the same scenario in which multiple nodes multicast the same data reply over the network.
In fact the situation is exacerbated when duplicate interests are multicasted and unsolicitated data is cached.

## Slide 6
Interest for /A
At t = 0ms a node multicasts interest /A.

## Slide 7
Reply for /A
At t = 10ms two nodes multicast data replies for interest /A
Reply for /A

## Slide 8
Interest for /A
At t = 10ms a second node also multicast interest /A
If the node cached the unsolicited data reply for /A it should satisfy the interest from its own cache but at t = 10ms it has not yet heard the data replies.

## Slide 9
Reply for /A
At t = 20ms potentially many nodes multicast data replies for interest /A
Reply for /A
At this point and assuming no loss this node already heard the reply at
t ~ 10ms.
Reply for /A
Reply for /A

## Slide 10: Interest Suppression Basics
The basic idea is to eavesdrop on multicasted interests for some amount of time before forwarding the interest.
Our initial design had every multicasted interest wait an independently randomized amount of time.
If the same interest was heard then the interest was sent to NFD with nextHopId = null face. This creates a PIT but does not forward the interest.
Interest suppression only needs to occur at endpoints. NFD's that are only forwarding interests do not change behavior.

## Slide 11
Interest for /A
At t = 0ms, node waits for 80ms before multicasting /A.

## Slide 12
Interest for /A
At t = 30ms blue node waits 100ms before multicasting /A.

## Slide 13
Interest for /A
At t = 80ms black node multicasts interest /A because it heard no duplicate interests.
Node hears the interest for /A and suppresses its own interest.

## Slide 14: Smarter Interest Suppression
The likliehood of duplicate multicasted interests occuring around the same time depends entirely on application behavior on the network.
  For instance, general file transfers there may a very small chance of two nodes downloading the same segment at the same time.
  We don't want to always apply interest suppression as it does add a per interest delay.

## Slide 15: Smarter Interest Suppression
Two timers are tracked. m_listen and m_suppress
For every multicasted interest the node listens for m_listen time for duplicate interests.
If a duplicate interest is heard then m_suppress is increased.
  Else m_suppress is decreased.
If m_suppress > 0, interests will follow the previous suppression scheme waiting a random amount of time from 0 to m_suppress.
Must be done on a per flow basis.
  Suppression of /A should not affect interests for /B for example.

## Slide 16
Outgoing Interest
Is m_suppress > 0?
Listen for duplicate interests for m_listen
Duplicate interest received?
Increase m_suppress.
Decrease m_suppress.
Wait for random time up to m_suppress.
Express interest
Duplicate interest received?
Suppress expressing outgoing interest.
yes
no
yes
no
no
yes

## Slide 17
Listen for m_listen time.
Node A
Other Nodes

## Slide 18
Listen for m_listen time.
Node A
Other Nodes
Listen for m_listen time.

## Slide 19
m_suppress increased
Listen for m_listen time.
m_suppress increased
Node A
Other Nodes

## Slide 20
m_suppress increased
Listen for m_listen time.
New interest. Wait up to m_suppress time.
m_suppress increased
Node A
Other Nodes

## Slide 21
m_suppress increased
Listen for m_listen time.
New interest. Wait up to m_suppress time.
m_suppress increased
Node A
Other Nodes

## Slide 22
m_suppress increased
Listen for m_listen time.
New interest. Wait up to m_suppress time.
m_suppress increased
Node A
Other Nodes
New interest. Wait up to m_suppress time.

## Slide 23
m_suppress increased
Listen for m_listen time.
New interest. Wait up to m_suppress time.
m_suppress increased
Node A
Other Nodes
New interest. Wait up to m_suppress time.
Duplicate interest received. Suppress this interest.

## Slide 24
m_suppress increased
Listen for m_listen time.
New interest. Wait up to m_suppress time.
m_suppress increased
Node A
Other Nodes
New interest. Wait up to m_suppress time.
Alternatively

## Slide 25
m_suppress increased
Listen for m_listen time.
New interest. Wait up to m_suppress time.
m_suppress increased
Node A
Other Nodes
New interest. Wait up to m_suppress time.
Alternatively
m_suppress increased
m_suppress increased

## Slide 26
m_suppress increased
Listen for m_listen time.
New interest. Wait up to m_suppress time.
m_suppress increased
Node A
Other Nodes
New interest. Wait up to m_suppress time.
Alternatively
m_suppress increased
m_suppress increased
New interest. Wait up to m_suppress time.

## Slide 27: Tracking Multicast Prefix Flows
Use self-learning to retrieve a prefix announcement.
Assign a MulticastSuppression forwarding strategy to this prefix
  Store m_supress and last_sent(?) as strategy info.
  Only affects interests from a local face to a multicast face. (need a backup strategy for other faces?)
  Needs to be able to know when to stop tracking a prefix and go back to the default forwarding strategy.
Perhaps application registration/deregistration is simpler?

## Slide 28: Suppression Window
Max m_supress and m_listen is the interest lifetime.
If a duplicate interest is recv'd outside of m_supress but after sending an interest then...
  Window may not be large enough.
  Other interest may have long propagation delay.
  Interest may have been expressed close to end of window.
If a duplicate interest is recv'd within m_suppress but after sending an interest then...
  Random delays were too close together.
  Interest may have been expressed before the start of the window.

## Slide 29: Data Reply Suppression
Multicasted data reply suppression follows the same scheme as interest suppression (basic) with a few caveats.
  There is less effect of interest timing. Two nodes could be downloading the same file at different segments. If there are two producers then there will still be two data replies for each node's segment interest.
  Forwarding nodes may have data cached and thus also need to participate in data reply suppression.
  If there is no need for data replies to be multicasted then a multicast/unicast switch is a better solution.

## Slide 30: Conclusion
Current method of Basic Interest Suppression was implemented at the application layer requiring prefixes to be registered.
Results showed double digit increases in goodput.
Current method of Data Reply Suppression implemented as a forwarding strategy and only applied to content store hits.
Results showed more than a two fold increase in goodput.
Combining both interest suppression and data reply suppression.
Results in almost three fold increase in goodput.

## Slide 31: Caveats
Both interest suppression and data reply suppression work at a per prefix level.
Content store replies present an issue since these NFD's don't have a priori knowledge of what prefix to perform data suppression on.
A posteriori knowledge can be obtained via a learning mechanism.
Nodes that exist outside the multicast group can't participate in suppression as they will not over hear interests or data replies.
Nodes at the borders may delay unicasting an interest to see if a multicasted data reply satisfies that interest.
Both consumers and producer apps can register the prefix with their NFD.